## Slide 1
Supporting UR Science Series: Lowering Costs at the Genomics Research Center Written by: Elizabeth Pritchett, Anthony Gaca, Jeffrey Malik Experiment Performed by: Phil Spinelli; Analysis by: Anthony Gaca
Introduction
As part of our ongoing efforts to optimize workflows and reduce costs for our community, we conducted a study comparing our standard-input mRNA and Total RNA library construction methods to assess whether reducing reagent volumes would impact data quality.
Experimental Details
Sample Type: Universal Human Reference (UHR) RNA.
Extracted from cell lines representing different human tissues
Pooled from 10 subjects
gDNA depleted
Includes low, medium, and high abundance gene transcripts
Input Concentrations:
25 ng
100 ng
Library Preparation Kits:
Experimental Results
Conclusion
Overall, all metrics are similar between full volume and reduced volume reactions for both mRNA and Total RNA Library preparations
  Genes detected
  Transcript Coverage
  Sample-to-sample correlation
  Reads assigned to transcripts
By implementing reduced reagent volumes, we achieve lower per-sample costs while adhering to the high-quality standards of the GRC
As part of our strategic goals for our community, we have more to come!
Library Prep and Volume | mRNA Full | mRNA Reduced | Total RNA Full | Total RNA Reduced
Avgerage Library Size (bp) | 340 | 341 | 391 | 383
Depth (M reads) | 30 | 30 | 50 | 50
Read Length (bp) | 2x150 | 2x150 | 2x150 | 2x150
*Genes Detected | 100ng: 27,246 25ng: 27,026 | 100ng: 27,442 25ng: 27,113 | 100ng: 31,599 25ng: 31,276 | 100ng: 31,020 25ng: 30,986
Kit Type | Approach
Stranded mRNA | Coding Transcriptome
Stranded Total RNA | Coding and non-coding Transcriptome
Sequencing performed using the NovaSeq X PLUS. *A minimum of 3 reads mapped to each gene was required for detection.

## Slide 2
Results
Transcript Read Coverage:
Figure 2: Reduced volume library preparations have even transcript coverage. Cumulative mapped-read depth at relative transcript positions as determined by QualiMap. Values are normalized to the overall number of mapped reads for each sample to account for varying sequencing depth.
Assignment to Genomic Features:
Figure 1: Consistent mapping of reads to genomic features with reduced library preparation volumes. Percent mapped reads assigned to each featureCounts category. Ambiguous indicates that a mapped read is associated with a region of transcript overlap. Unassigned indicates that a mapped read is not associated with a protein-coding region. Total RNA libraries capture non-coding transcripts leading to higher unassigned read levels.
Sample Correlation by Reaction Volume:
Figure 3: Reduced volume library preparations maintain near perfect transcript abundance correlation. Correlation plots of log10(CPM) normalized transcript count values between full and reduced volume library preparations. Regression lines and R2 values are derived using a standard linear model.
Supporting UR Science Series: Lowering Costs at the Genomics Research Center Written by: Elizabeth Pritchett, Anthony Gaca, Jeffrey Malik Experiment Performed by: Phil Spinelli; Analysis by: Anthony Gaca